## Slide 1: 模糊集合及其應用 Fuzzy Set and Its Applications
張智星
台灣大學資訊系教授/玉山金控科技長
jang@mirlab.org, http://mirlab.org/jang

## Slide 2: Fuzzy Sets（模糊集合）
Fuzzy sets
  Sets with fuzzy boundaries（邊界模糊的集合）
  Example: A = Set of tall people （高的人所成的集合）
Heights
(cm)
170
1.0
Crisp set A
Membership
Function
（歸屬函數）
Heights
(cm)
170
180
0.5
0.9
Fuzzy set A
1.0

## Slide 3: Membership Functions（歸屬函數）
MFs
  Subjective measure（主觀的量測）
  Not probability（和機率無關）
  AKA possibility（又稱為possibility）
MFs
Heights
(cm)
180
.5
.8
.1
“tall” in Taiwan
“tall” in the US
“tall” in NBA

## Slide 4: Approximate Reasoning (A Branch of AI) 近似推理（人工智慧分支）
Types of uncertainty (不確定性的類別)
  Probability  客觀的事實
  Possibility  主觀的認定
Goal of approximate reasoning
  Reasoning and aggregation of uncertainties
Example
Poisonous with a
probability of 0.2
Poisonous with a
possibility of 0.2

## Slide 5: Fuzzy If-Then Rules（模糊規則）
Mandani style
  If pressure is high, then volume is small.
  若壓力大，則容量小。
Sugeno style
  If speed is median, then resistance = 5*speed.
  若速度適中，則阻力是速度的五倍。
high
small
medium
resistance = 5*speed

## Slide 6: Fuzzy Inference Systems (FIS，模糊推論系統)
If speed is low then resistance = 2
If speed is medium then resistance = 4*speed
If speed is high then resistance = 8*speed
Rule 1: w1 = 0.3; r1 = 2
Rule 2: w2 = 0.8; r2 = 4*2
Rule 3: w3 = 0.1; r3 = 8*2
Speed
2
w1=0.3
w2=0.8
w3=0.1
low
medium
high
Resistance = S(wi*ri) / Swi
= 7.12
MFs
Rule
base

## Slide 7: First-order Sugeno FIS
Rule base（規則庫）
  If X is A1 and Y is B1 then Z = p1*x + q1*y + r1
  If X is A2 and Y is B2 then Z = p2*x + q2*y + r2
Fuzzy reasoning（模糊推理）
A1
B1
A2
B2
x=3
X
X
Y
Y
y=2
w1
w2
z1 =
p1*x+q1*y+r1
z =
z2 =
p2*x+q2*y+r2
w1+w2
w1*z1+w2*z2
P

## Slide 8: FIS的建構與應用
FIS的建構
  以專家的知識來建構  模糊專家系統（fuzzy expert system）
  以類神經網路的方式來建構  神經模糊系統（neuro-fuzzy system）
FIS的各種應用
  若應用於控制系統，則成為模糊邏輯控制器（FLC, fuzzy logic controller）
  若應用於分類或迴歸，則變成分類器或迴歸器

## Slide 9: ANFIS: Adaptive Neuro-Fuzzy Inference System
Fuzzy reasoning
ANFIS
A1
B1
A2
B2
w1
w2
z1 =
p1*x+q1*y+r1
z2 =
p2*x+q2*y+r2
z =
w1+w2
w1*z1+w2*z2
x
y
A1
A2
B1
B2
P
P
S
S
/
x
y
w1
w2
w1*z1
w2*z2
Swi*zi
Swi
z

## Slide 10: 模糊邏輯控制器：洗衣機的應用
洗衣機的模糊控制
  感測器：稱重器、布料感測器、溫度計、水質感測器等
  控制量：進水量、水溫、洗滌時間、脫水速度等
  效益：省電、省水、保護衣服
References:
https://www.samsung.com/in/support/home-appliances/what-is-fuzzy-logic-in-a-washing-machine/
https://onsitego.com/blog/fuzzy-logic-means-washing-machine/
https://iopscience.iop.org/article/10.1088/1757-899X/384/1/012044

## Slide 11: 模糊邏輯控制器：冷氣機的應用
冷氣機的模糊控制
  感測器：溫度、濕度、露點溫度、壓力、伏特數等
  控制量：壓縮機轉速、風扇轉速、操作模式、翅片轉速等
  效益：省電、更快達到舒適溫度
References:
https://www.ijcaonline.org/research/volume126/number15/sobhy-2015-ijca-906083.pdf