## Slide 1: ML-based Side-Channel Attack for POI Selection in Thermal Emission
J.-S. Roger Jang (張智星)
MIR Lab, CSIE Dept.
National Taiwan University
jang@mirlab.org, http://mirlab.org/jang

## Slide 2: Project Summary
Our goals
  Decrypt AES-128 using thermal map (non-invasive)
  Locate leakage tiles on a chip
Assumptions
  Plaintext (input) and encrypted text (output) are known.
  Large amount of I/O data are available.
Methods
  AES-128 encrypts within a 4x4 matrix
  Build 16 ML models, each with 256 classes
    Input: thermal map
    Output: value of a byte, 0~255
Byte 0 | Byte 4 | Byte 8 | Byte 12
Byte 1 | Byte 5 | Byte 9 | Byte 13
Byte 2 | Byte 6 | Byte 10 | Byte 14
Byte 3 | Byte 7 | Byte 11 | Byte 15

## Slide 3: Flowchart of Proposed Approaches
Preprocessing
Standard deviation
POI selection
Check invalid inputs
Sharpen images
Attack model training
Calculate standard deviation for each pixel
Lineup model
Image heatmap model
Best POI number model
Side-channel attack
Evaluation metrics
Rank
Require traces to disclose (RTD)
Top-5 accuracy
Leakage tiles identification
Monitor the changes of loss response curve
Loss
Sequential forward selection

## Slide 4: Dataset
Full-chip thermal images
  Average temperature during an encryption process using a given plaintext (based on Ansys’ simulation tool)
  Size: 201 x 201 pixels, 1 pixel= 10 μm x 10 μm
  Amount: 20,000 images, 17,000/3,000 for training/test
Plaintext and key
  20,000 different plaintext, such as
    [64, 4E ,7F ,36, C3, D6, 6B, 78, 88, C6, 93, 87, F4, 33, A4, 0E]
  A single key
    [00, 11, 22, 33, 44, 55, 66, 77, 88, 99, AA, BB, CC, DD, EE, FF]
Tile: each pixel
Trace: each image

## Slide 5: Operating POI in a Thermal Map
Operating POI (points of interest)
  16 tiles where AES encryption is processed
  Most leakage tiles for each byte
    To be identified by machine learning
AES-128 SoC design[1],
with 16 operating POI
Byte
0
Byte
3
Byte
4
Byte
14
Byte
15
Byte
5
Byte
10
Byte
2
Byte
8
Byte
12
Byte
11
Byte
6
Byte
1
Byte
7
Byte
13
201pixels
Thermal map
Detailed locations of
16 operating POI
Byte 0 | Byte 4 | Byte 8 | Byte 12
Byte 1 | Byte 5 | Byte 9 | Byte 13
Byte 2 | Byte 6 | Byte 10 | Byte 14
Byte 3 | Byte 7 | Byte 11 | Byte 15

## Slide 6: Tile Selection based on Standard Deviation
Select N tiles based on their standard deviation (within 17,000 images)
Standard deviation map
0
2
3
4
5
6
7
8
9
10
11
12
13
14
1
15
All 16 operating-POIs are selected when N=200.

## Slide 7: Evaluation Metrics
Cross entropy loss
  Use validation loss to choose the best number of POI
Ranking
  Compute all labels’ log probabilities for each of 3,000 traces
  Transform from label to key and obtain key’s log probability
  Sort correct key’s rank among all candidates while accumulating the log probability from trace 1 to 3,000.
Correct key’s rank
Key rank stays 0 from 318 to 3000
RTD (required traces to disclose)
  Min no. of traces required for a correct key to stay at rank 0 in a stable state  The less, the easier to crack a byte.

## Slide 8: POI Search: Lineup Selection
Objective
  POI search by lineup selection via MLP
Result
  200  137 POI for byte 0
Chart: Byte0 POI number search result build with MLP
Not able to crack within 3000 traces
Best point where the loss is the lowest
Remark: For trials that can not find the key within 3,000 traces
(ex: before 49 POI), its RTD is recorded as 3,000 + correct key rank

## Slide 9: POI Search: Sequential Forward Selection
Objective
  POI search by sequential forward selection via MLP
Result
  137  8 POI for byte 0
Chart: Byte0: validation loss response
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Val_loss | 5.5457 | 5.5218 | 5.4924 | 5.4847 | 5.4805 | 5.4793 | 5.4744 | 5.4741
POI59
(94, 162)
POI123
(93, 161)
POI55
(93, 162)
POI140
(88, 150)
POI118
(81, 114)
POI186
(91, 163)
POI87
(94, 166)
POI49
(94, 161)
Operating POI for byte0 is No. 49
with coordinate (94, 161)

## Slide 10: Summary
Conclusions
  Location depended side-channel attack
    Decrypted AES-128 using full-chip temperature image and selected POI
  Leakage points detection
    Best POI number search gives precise leakage tiles’ location
Future work
  Other efficient classifiers
  From heuristics to exhaustive search of POI
    200  137 8  ???
  Test attacking performance with other filters
  Test with different types of emission